## Slide 1: Quantitative Magnetization Transfer Imaging Made Easy with
Open Source Software for qMTI Data Simulation, Analysis and Visualization
ISMRM 2016, Singapore
e-poster #3205
Cabana, J.-F.1, Gu, Y.2, Boudreau, M.3, Levesque, I. R.4, Atchia, Y.5, Sled, J. G.5,6, Narayanan, S.3, Arnold, D. L.3, Pike, G. B.3,7, Cohen-Adad, J.8, Duval, T.8, Vuong, M.-T.8 and Stikov, N.8,9
1University of Montreal, Montreal, QC, Canada; 2NeuroRX, Montreal, QC, Canada; 3Montreal Neurological Institute, Montreal, QC, Canada; 4McGill University, Montreal, QC, Canada; 5University of Toronto, Toronto, ON, Canada; 6Hospital for Sick Children, Toronto, ON, Canada; 7University of Calgary, Calgary, AB, Canada; 8Ecole Polytechnique, Montreal, QC, Canada; 9Montreal Heart Institute, Montreal, QC, Canada
qMTLab

## Slide 2: What is qMTLab
qMTLab is a set of tools with a graphical user interface (GUI) for quantitative magnetization transfer imaging (qMTI) data fitting, visualization, analysis and simulation
  Open source
  Flexible
  Easy to use
  Built in MATLAB
  For more info on qMTI and qMTLab, see our 2016 paper [1]
  Cabana et al (2016). Quantitative magnetization transfer imaging made easy with qMTLab : Software for data simulation, analysis, and visualization. Concepts Magn. Reson.. doi: 10.1002/cmr.a.21357
/17

## Slide 3: Why we developed qMTLab
Quantitative magnetization transfer imaging (qMTI) offers a distinct contrast mechanism sensitive to tissue molecular composition
  Allows extraction and quantification of distinct tissue characteristics with high reproducibility and specificity to macromolecular content
However, its use has been mostly restricted to researchers that have developed these methods, in part due to the need to write complicated in-house software for modeling and data analysis.
Our objective
  By providing free software that gives end users a simple and easy to use graphical interface, we hope to make qMTI accessible to a greater number of investigators and facilitate the development, evaluation and optimization of acquisition protocols and analytical models.
/17

## Slide 4: What is magnetization transfer imaging
Magnetization transfer (MT) refers to the interaction between freely moving protons and restricted protons bound to macromolecules
By modeling the exchange process between the liquid and the macromolecular pool of protons, qMTI allows the measurement of precise information about tissue composition
  Fraction of the restricted to free pools
  MT exchange rate
  Relaxation rates
/17

## Slide 5: The two-pool model
Most qMTI methods are based on the two-pool tissue model [2], characterised by seven independent parameters:
  F - pool size ratio ( = M0r/M0f)
  kf - forward exchange rate
  R1f - free pool longitudinal relaxation rate ( = 1/T1f)
  R1r - restricted pool longitudinal relaxation rate ( = 1/T1r)
  T2f - free pool transverse relaxation time
  T2r - restricted pool transverse relaxation time
  M0f - free pool equilibrium magnetization
Two additional dependent parameters
  kr - reverse exchange rate ( = kf/F)
  M0r - restricted pool equilibrium magnetization ( = F x M0f)
A signal equation is fitted to the data to extract these parameters
[2] R. M. Henkelman et al., MRM, 1993
/17

## Slide 6: Acquisition methods
qMTLab currently supports the most widely used acquisition methods and analytical models
MT-SPGR
  Combines off-resonance pulsed saturation of the restricted pool with an SPGR readout [3]
  Vary MT pulse duration (tmt) and power (αmt)
SIR-FSE
  Uses a selective inversion recovery sequence followed by a fast spin echo readout [4]
  Vary inversion time (ti) and/or delay time (td)
MT-bSSFP
  bSSFP induces a significant MT effect when large flip angles and short TR are used [5]
  Vary flip angle (α) and RF pulse duration (trf)
MT-SPGR
SIR-FSE
MT-bSSFP
[3] Pike, MRM, 1996.; [4] Gochberg et al. MRM, 1999; [5] Bieri and Scheffler, MRM, 2007
/17

## Slide 7: Data fitting with qMTLab
qMTLab provides a convenient interface to fit your qMTI data and visualize the parameters maps
First define or load your acquisition protocol parameters, using the Options panel
  Once set, protocol can be saved for later use
  Useful tip : Replace the “DefaultProt.mat” file with your preferred protocol to have it automatically loaded when you launch qMTLab
/17

## Slide 8: Easy configuration of fitting options
Use default fitting options or experiment with your own
  Choose the model you want to use
  Select the lineshape of the restricted pool (Gaussian, Lorentzian, SuperLorentzian)
  Keep certain parameters fixed
  R1r : Fix to a certain value, set = R1f, or fit
  Set starting search point
  Define lower and upper bounds
  Save your preferences for later use
  Useful tip : Replace the “DefaultFitOpt.mat” file with your preferred fitting options to have them automatically loaded when you launch qMTLab
/17

## Slide 9: Importing your data
Load your qMTI data
Preview your maps for quality control
Test the fitting on selected voxels
Hit the « Fit Data » button
Results are saved in your working directory as a single .mat file and separate maps as .nii files
  Useful tip : Put all your files in the same directory and select it as your « Work dir. » -> All the files,protocol and fitting options are loaded automatically
/17

## Slide 10: Fit results visualization
View the fitted parameters maps directly in qMTLab
  Choose parameter to display
  Change color map (color scheme, limits)
  View parameter distribution histogram
  View selected voxel value
  View selected voxel data + fitted curve
  Useful tip : When working with 3D data, click « Open viewer » to open a viewer with 3 simultaneous orthogonal views and easier volume navigation
/17

## Slide 11: Data simulation
The simulation part of qMTLab is useful for researchers to:
  Generate synthetic qMTI data
  Evaluate how well the different methods/models perform under known ground-truth
  Determine the most appropriate acquisition parameters
  Evaluate how fitting options and constraints impact the results
Three modes of simulation:
Single Voxel Curve
Sensitivity Analysis
Multi Voxel Distribution
/17

## Slide 12: Single Voxel Curve
Simulate MT data for a single voxel
Evaluate various acquisition protocols, the performance of the model and fitting options
The model is fitted and a plot displays
  Raw data
  Data with added Gaussian noise
  Fitted curve
Input MT parameter values, fitted parameters values and percentage difference are listed in a table
  Useful tip : You can change fitting options or generate a new set of noisy data and re-fit without having to run the simulation again by simply clicking on « Update Fit »
/17

## Slide 13: Sensitivity Analysis
Systematically vary one MT parameter at a time while keeping the others fixed
  Select which parameters to vary
  Set minimum/maximum values and step size
Gaussian noise is added and the fit is run multiple times (set with « # of runs »)
Select the independent and dependant variables to see how the variation of one affects the other
/17

## Slide 14: Multi Voxel Distribution
Any parameter combination is allowed to be varied simultaneously
  Choose the number of voxels
  Select which parameters to vary
  Set mean value and variance for each parameter
Analyze results in a number of ways
  Histograms
  Scatter plots of input vs fitted parameters
  Error histograms
  Bar graphs (RMSE, NRMSE, MPE)
/17

## Slide 15: Integrating qMTLab in your pipeline
No complicated installation procedure or dependencies
  Just add qMTLab folder to your MATLAB path
Use in MATLAB scripts
  Fit = FitData(data, Protocol, FitOpt, Method)
    data is a structure with fields 'MTdata', and optionally 'Mask','R1map','B1map','B0map'
    Protocol is a protocol structure saved from the qMTLab Options panel
    FitOpt is a fitting options structure saved from the qMTLab Options panel
    Method selects ‘SPGR’, ‘SIRFSE’ or ‘bSSFP’
qMTLab GUI can load .mat or .nii files
Includes external tools for file conversion
  Tools for NIfTI and ANALYZE image (by Jimmy Shen)
  DICOM to NIfTI converter, NIfTI tool and viewer (by Xiangrui Li)
/17

## Slide 16: What’s coming up
Additional MT methods
  MTsat
  MTR
Parallel computing support
  Faster data fitting / simulation
Your own contribution
  Comments, suggestions and improvements are welcome on the GitHub repository
  For more info on qMTI and qMTLab, see our 2016 CMR paper
  Cabana et al (2016). Quantitative magnetization transfer imaging made easy with qMTLab : Software for data simulation, analysis, and visualization. Concepts Magn. Reson.. doi: 10.1002/cmr.a.21357
Download qMTLab for free :
https://github.com/neuropoly/qMTLab/
/17

## Slide 17: References
[1] J.-F. Cabana, Y. Gu, M. Boudreau, I. R. Levesque, Y. Atchia, J. G. Sled, S. Narayanan, D. L. Arnold, G. B. Pike, J. Cohen-Adad, T. Duval, M.-T. Vuong, and N. Stikov, “Quantitative magnetization transfer imaging made easy with q MTL ab : Software for data simulation, analysis, and visualization,” Concepts Magn. Reson.. doi: 10.1002/cmr.a.21357.
[2] R. M. Henkelman, X. Huang, Q. S. Xiang, G. J. Stanisz, S. D. Swanson, and M. J. Bronskill, “Quantitative interpretation of magnetization transfer,” Magn Reson Med, vol. 29, no. 6, pp. 759–766, 1993.
[3] G. B. Pike, “Pulsed magnetization transfer contrast in gradient echo imaging: A two-pool analytic description of signal response,” Magn. Reson. Med., vol. 36, no. 1, pp. 95–103, 1996.
[4] D. F. Gochberg, R. P. Kennan, M. D. Robson, and J. C. Gore, “Quantitative imaging of magnetization transfer using multiple selective pulses,” Magn Reson Med, vol. 41, no. 5, pp. 1065–1072, 1999.
[5] O. Bieri and K. Scheffler, “Optimized balanced steady-state free precession magnetization transfer imaging,” Magn Reson Med, vol. 58, no. 3, pp. 511–518, 2007.
Contact info: jean-francois.cabana@umontreal.ca
/17